## Slide 1: Educational Platforms &Frameworks for Learning AI on FPGA Hardware
Mohamed Abdo
Hamm-Lippstadt University of Applied Sciences
Prof. Dr. –Ing. Ali Hayek
[08.12.2026]

## Slide 2: Motivation
Skills Acquired?

## Slide 3: What is FPGA-AI?
1- Standalone FPGAs:
Programmable Logic Blocks
Thousands/millions of identical units
Basic digital components: LUTs, flip-flops, gates
Building blocks for any digital circuit without new silicon
Programmable Interconnects
  Re-routable wiring network
Connects logic blocks in any configuration
Enables custom circuit pathways
Hardened Components (Modern FPGAs)
Fixed-function blocks for efficiency:
  DSP slices: Optimized math operations
  Block RAM (BRAM): High-speed memory
  AI Engines: Dedicated neural network hardware (AMD Versal)
  Unlike:
CPU: Fixed hardware architecture, programmed with software
GPU: Massively parallel, but still fixed-architecture processor
FPGA fully reconfigurable

## Slide 4: What is FPGA-AI?
2- SoC FPGA
  Hybrid Architecture: ARM processors + FPGA fabric on single chip
  Power Efficiency: FPGA activates only needed logic
  Split Processing: CPU handles software, handles acceleration
  Zynq UltraScale+ MPSoC
3- High-End FPGA: Data Center Acceleration(Alveo)
  Huge FPGAs: Largest capacity available
  High-Bandwidth Memory (HBM): (16-32GB) with 460+ GB/s bandwidth, ultra-fast access

## Slide 5
Flexibility & Reconfigurability
  Update hardware architecture as AI models evolve
  Ideal for rapidly changing algorithms
  Deploy different models to same hardware at different times
Parallelism:
  Design circuits with hundreds/thousands of parallel elements
  All elements work simultaneously on different data parts
  Handles architectures difficult for CPUs/GPUs to parallelize
  Memory-augmented neural networks (MANNs), which in clude memory networks which is difficult to parallelize on CPUs or GPUs. [2]
Low Latency:
  Data flows directly through custom circuits
  Minimal processing overhead. [2]
  Crucial for real-time applications (medical, predictions)
Power Efficiency:
  Custom circuits perform exact operations needed
  No wasted energy on fetching/decoding generic instructions
  And Deep neural networks (DNNs) require more computing power and storage than most mobile devices can provide
Custom Datapaths:
  Design exact bit-width needed (e.g., 8-bit for quantized models)
  Avoid waste of generic 32-bit floating-point units in CPUs/GPUs.
  Optimize for specific model requirements

## Slide 7: Quantization & Deployment FLOW
Quantization: Convert 32-bit floats → 8-bit integers
100 MB → 25 MB (75% reduction)
Result: ~4x smaller model, ~2-4x faster, minimal accuracy loss

## Slide 8: Hls4ml Framework
hls4ml (High-Level Synthesis for Machine Learning)
  Open-source framework for converting ML models to FPGA firmware
  Specializes in neural network deployment on FPGAs
  Enables high-performance, low-latency FPGA inference
  Used by researchers and engineers for efficient model deployment

## Slide 9: Datasets & AI projects:
mnist | TensorFlow Datasets
CIFAR-10 and CIFAR-100 datasets

## Slide 10: PYNQ framework
[4]
Zynq™
Zynq UltraScale+™
Kria™
Alveo™ accelerator boards

## Slide 11: DPU
DPU = Deep Learning Processing Unit (Xilinx IP)
  Tiny low-power accelerator running directly on FPGA
  Customizable architecture for different AI workloads
  Massive parallelism for:
    conv layers
    pooling
    batch normalization
    activation functions
  Lower latency
  Lower power consumption
  Real-time performance on edge AI devices
  20×–100× faster vs pure ARM CPU inference.
How it fits into PYNQ:
Integration with PYNQ Framework
Run AI inference using Python notebooks
No HDL or Vitis AI C++ coding required
Load a bitstream that includes the DPU
Use pre-built Python APIs to:
  Load AI models (.xmodel format)
  Feed input tensors
  Receive inference outputs
[5]

## Slide 12: Vitis AI framework
Xilinx/Vitis-AI: Vitis AI is Xilinx’s development stack for AI inference on Xilinx hardware platforms, including both edge devices and Alveo cards.

## Slide 13: Recommended Families with Vitis AI
Chip: Zynq UltraScale+ ZU3EG
Category : Edge AI
Features: WiFi/BT

## Slide 14: Intel OpenVINO framework
OpenVINO 2025.4 — OpenVINO™ documentation — Version(2025)

## Slide 15: Recommended Families with OpenVINO

## Slide 16: FINN Framework
Xilinx/finn: Dataflow compiler for QNN inference on FPGAs

## Slide 17: SensiML – Picolo AI OS framework
RISC-V processor cores (not ARM)
RISC-V-CPU Layout
Arm Cortex-M Processor

## Slide 18: Recommended Families with Picolo AI

## Slide 19: How to Get Started with FPGA AI?

## Slide 20
QUESTIONS & DISCUSSION
Let's build the future of FPGA-AI education together!
Thank You

## Slide 21: References
Xilinx/Vitis-AI: Vitis AI is Xilinx’s development stack for AI inference on Xilinx hardware platforms, including both edge devices and Alveo cards.
IEEE Xplore Full-Text PDF:
hls4ml - CMS Machine Learning Documentation
[4] PYNQ supported boards and PYNQ pre-built images | PYNQ
[5] DPU Configuration • DPUCZDX8G for Zynq UltraScale+ MPSoCs Product Guide (PG338) • Reader • AMD Technical Information Portal